## Slide 1: Modeling kernels

## Slide 2: Kernels on the market
ACIS
Parasolid
CGM
C3D
RGK
SMLib
OpenCascade

## Slide 3: Exact reps

## Slide 4: Inexact reps

## Slide 5: ISO 10303, part 42
This part of ISO 10303 [part 42] specifies the resource constructs for the explicit geometric and topological representation of the shape of a product. The scope is determined by the requirements for the explicit representation of an ideal product model; tolerances and implicit forms of representation in terms of features are out of scope.

## Slide 6: Why B-Rep?
Boundary modelers are currently dominating the CAD/CAM market. Why is it so? The short answer to this question as defined in [5]:
WYSIWYG: every EDGE and FACE displayed on the screen is explicitly held in the model’s data structure, making the editing and interrogation of objects straightforward. This may appear to be a trivial point but it makes the attachment of attributes, such as machining tolerances, to elements very easy.

## Slide 7: But…
It is extremely hard to build a robust modeler. In general, the following criteria are used to assess every single algorithm:
Accuracy
Robustness
Efficiency
(*) Intelligence
Moreover, there should be ENOUGH algorithms to allow for general-purpose geometric modeling.

## Slide 8: Meet OpenCascade

## Slide 9: Meet OpenCascade
http://quaoar.su/blog/page/opencascade-overview

## Slide 10: What is OpenCascade?
  «Although there are facilities for displaying graphics in Open CASCADE, the real function of the library is to do the math.
  There are dozens of graphics libraries (if not hundreds), but there are very few solid modeling libraries, and Open CASCADE is the only open source solid modeler.»
  [COMMUNITY]

## Slide 11: Modules

## Slide 12: Modules
or

## Slide 13: Modules
or
Where to find what in the library?

## Slide 21
Foundation Classes

## Slide 22
Foundation Classes // Math
Linear algebra

## Slide 23
Foundation Classes // Math
Linear algebra
  Solvers

## Slide 24
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors

## Slide 25
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD

## Slide 26
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization

## Slide 27
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization
  Newton, BFGS, FRPR, Powell

## Slide 28
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization
  Newton, BFGS, FRPR, Powell
  PSO

## Slide 29
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization
  Newton, BFGS, FRPR, Powell
  PSO
Approximation and interpolation

## Slide 30
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization
  Newton, BFGS, FRPR, Powell
  PSO
Approximation and interpolation
  By points or sections (discrete data)

## Slide 31
Foundation Classes // Math
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization
  Newton, BFGS, FRPR, Powell
  PSO
Approximation and interpolation
  By points or sections (discrete data)
  By continuous function (e.g. from offset surface to polynomial)

## Slide 32
Modelling

## Slide 33
Modelling

## Slide 34
Modelling

## Slide 35
Modelling

## Slide 36
Modelling

## Slide 37
Modelling

## Slide 38
Modelling

## Slide 39
Modelling

## Slide 40
Modelling

## Slide 41
Modelling

## Slide 42
Modelling

## Slide 43
Modelling

## Slide 44
Modelling

## Slide 45
Mesher

## Slide 46
Mesher

## Slide 47
Mesher

## Slide 48
Mesher

## Slide 49
Data Exchange

## Slide 50
Data Exchange

## Slide 51
Data Exchange

## Slide 52
OCAF

## Slide 53
OCAF

## Slide 54
OCAF

## Slide 55
Visualisation

## Slide 56
In the file system
Package 1 / Class 1
Package 1 / Class 2
Package 2 / Class 1
Package 2 / Class 2
…

## Slide 57
More reading
An Introduction to Solid Modeling. M. Mantyla. 1988.
The NURBS Book. L. Piegl, W. Tiller.
Solid Modelling and CAD Systems. How to Survive a CAD System. I. Stroud. 2011.
Open Cascade Technology Overview // URL: http://quaoar.su/blog/page/opencascade-overview
3D Modelling with ACIS. Corney J.R., Lim T. 2001.

## Slide 58: Math support
Linear algebra
  Solvers
  Eigen values & vectors
  SVD
Optimization
  Newton, BFGS, FRPR, Powell
  PSO
Approximation and interpolation
  By points or sections (discrete data)
  By continuous function (e.g. from offset surface to polynomial)

## Slide 59: Modeling
Surface
  Kinematic surfaces
  Skinning
  …
Solid
  Prism
  Draft
  Thin-walled solid
  Booleans
  …

## Slide 60: Data exchange
Format:
  Exact: STEP (ISO 10303), IGES
  Polygonal: STL, VRML, OBJ, glTF
Data:
  Geometry
  Meta (assemblies, colors, names, attributes, etc.)

## Slide 61: In filesystem
Package 1 / Class 1
Package 1 / Class 2
Package 2 / Class 1
Package 2 / Class 2
…

## Slide 62: Build with CMake
1
2
3
4
5

## Slide 63: Interesting reading
An Introduction to Solid Modeling. M. Mantyla. 1988.
The NURBS Book. L. Piegl, W. Tiller.
Solid Modelling and CAD Systems. How to Survive a CAD System. I. Stroud. 2011.
Open Cascade Technology Overview // URL: http://quaoar.su/blog/page/opencascade-overview
3D Modelling with ACIS. Corney J.R., Lim T. 2001.

## Slide 64: Hello World

## Slide 65: Entry point: Draw
Tcl interpreter with extensions
Access to the entire modeling API
Rapid prototyping

## Slide 66: Basic commands
> pload ALL
> box a 1 1 1
> axo; fit
> vinit
> vdisplay a
>> f
>> s
>> Ctrl + RMB
1
2
3

## Slide 67: Prismatic block
proc buildBlock {resname L0 B0 a1Deg a2Deg height} {
global $resname
set Pi 3.1415926535897931
# Design variables.
set a1 [expr $a1Deg.*$Pi/180.]
set a2 [expr $a2Deg.*$Pi/180.]
set V1x [expr -$L0/2 - tan($a1)*$B0/2]
set V1y 0
set V2x [expr $L0/2 + tan($a2)*$B0/2]
set V2y 0
set V3x [expr $L0/2 - tan($a2)*$B0/2]
set V3y $B0
set V4x [expr -$L0/2 + tan($a1)*$B0/2]
set V4y $B0
# Build topology.
vertex V1 $V1x $V1y 0.
vertex V2 $V2x $V2y 0.
vertex V3 $V3x $V3y 0.
vertex V4 $V4x $V4y 0.
#
edge e1 V2 V1
edge e2 V1 V4
edge e3 V4 V3
edge e4 V3 V2
wire w e1 e2 e3 e4
mkplane f w
#
prism $resname f 0 0 $height
}
# pload ALL
# source C:/Work/lendlease/demo-ssv/create-block-01.tcl
# buildBlock b 130 60 20 45 30
# top; fit
V1
V2
V3
V4

## Slide 68: Similar things
ACIS Scheme AIDE
C3D Test Application
It is never a CAD-system, just a console or test app.

## Slide 69: How to build a simple app?
Options
  Your main() function // No visualization
  Executable with Draw // .exe
  Plugin for Draw // .dll

## Slide 70: Understanding B-rep

## Slide 71: Geometry vs Topology
“To solve many of geometric problems we do not need to know spatial information but what is required to be known is neighborhood or connectivity information termed as topology.” Sandip Jadhav

## Slide 72: ISO 10303-42 says
The geometry … is exclusively the geometry of parametric curves and surfaces. It includes the curve and surface entities and other entities, functions and data types necessary for their definition. A common scheme has been used for the definition of both two-dimensional and three-dimensional geometry.
The topology … is concerned with connectivity relationships between objects rather than with the precise geometric form of objects. This clause contains the basic topological entities and specialised subtypes of these. In some cases the subtypes have geometric associations. Also included are functions, particularly constraint functions, and data types necessary for the definitions of the topological entities.

## Slide 73: Geometry vs Topology

## Slide 74: Geometry vs Topology
Geometry = real locations
Topology = connections

## Slide 75: Geometry vs Topology

## Slide 76: Geometry vs Topology

## Slide 77: Geometry vs Topology

## Slide 78: Geometry vs Topology

## Slide 79: Geometry vs Topology

## Slide 80: Geometry vs Topology

## Slide 81: Geometry vs Topology

## Slide 82: Geometry vs Topology

## Slide 83: Geometry vs Topology
EDGE
VERTEX
FACE

## Slide 84: Реализация в OpenCascade
TopoDS
Geom
Geom2d

## Slide 85: OpenCascade vs ACIS

## Slide 86: Assemblies and data exchange

## Slide 87: Assemblies
Geometry: TopoDS
Assemblies and meta: XDE/OCAF